## Slide 1: Analysis of Regression Models for estimating the main bearing loads of wind turbines
Master Thesis
Mithun Nagesh Shet
Aachen, 12.08.2022

## Slide 2: Structure
6
Motivation
Background
Objective
Methodology
Result Study
Summary and Outlook
1
4
3
5
6
2
5
4
3
2
1
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 3: MOTIVATION
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 4: Motivation
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Source : Office of energy efficiency and renewable energy
Wind is set for largest increase in renewable energy generation growing by 275TW by 2021.
The trend shows that there is substantial increase in diameter of turbine blades and size of hub every decade by an amount of 40 percent every decade.
This increased size has significantly increased the torque and non torque loads.

## Slide 5: Motivation
Under ideal conditions, lifespan of wind tubine is around 20 years.
In actual , the wind turbine lasts for about 6 years.
Reason:
Fatigue mechanism
Wear and tear due to bearing misalignment
Bearing unseating, skewing and sliding due to high axial to radial loads.
Solution:
Load monitoring system to monitor loads and send signals prior to observed failures.
High Operation cost and less service life
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 6: BACKGROUND
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 7: Background
Currently strain based load estimation is used.
Measurement based on linear relationship between strains and loads.
Vulnerable to calibration error and signal drift.
Limited lifetime.
A better technology is necessary which is long-lasting and robust.
Strain Gauge
Strains
Main Bearing loads
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Machine Frame
Tower and Foundation
Rotor Blades
Source : Leine Linde Systems

## Slide 8: OBJECTIVE
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 9: Objective
Replacing the traditional method of using strain gauges by machine learning models.
Training, building and testing the models from displacement signals recorded by Eddy current sensors to predict loads.
Checking robustness of models to errors like Gain error, Offset error and sinewave error.
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Shaft Rotation (radians)
Gain
Error
Value
Offset
Error
Value
Offset Error (%)
0
5
Gain Error (%)
20%
0
-1
Amplitude
0
Ideal characteristic curve
Error
+1
Model Robustness
ML Model
Displacements
Main Bearing loads
Strain gauge for measuring bending moments
Linear variable differential transformer
Eddy current sensor
Strain gauge for measuring torque

## Slide 10: METHODOLOGY
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 11: Methodology
Load-time series input
Moderate Turbulence data
Test Data
Test Data
Machine Learning Models
Training Data
Model Evaluation
Low and High turbulence data
Displacement
Displacement
True Main Bearing loads
Predicted
Loads
eMBS model
Test Bench
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 12: EDA and Feature Engineering
EBT
ANN
LPR
TM
EDA
GPR
SVR
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Variables study
Outlier Detection
LB_Uz
FB_Uz
Normalization
Performance of regression models depend on quality of data and outliers can lead to high variance.
The training data was split in 80% for training and 20 % for validation.
The data was normalized using Z-score method.

## Slide 13: Linear and Polynomial Regression
Simple model and used as reference.
Residual error range
-120kN to +180kN.
EBT
ANN
LPR
TM
EDA
GPR
SVR
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Best Fit Line
x
y
Best Fit Line
x
y
Linear Regression for FB_Fx
Polynomial Regression for FB_Fx
Residual error range -100kN to +100kN.

## Slide 14: Regression Tree Model
Flexibility to capture nonlinear predictor-response relationship.
Minimum leaf size set at 35 to 40 for balanced fit.
Residual error varying between ±110kN with high density points found at around ±25kN
EBT
ANN
LPR
TM
EDA
GPR
SVR
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Decision Node
Root node
Terminal Node
Splits

## Slide 15: Support Vector Regressor
EBT
ANN
LPR
TM
EDA
GPR
SVR
Consists of Є tube which reformulates the optimization problem to find best tube that approximates continuous valued function.
The kernel was set as polynomial of order 2.
The residual error varied between ±120kN with high density of points seen around ±35kN.
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 16: Gaussian Process Regressor
Gaussian process regression (GPR) models are nonparametric kernel based probabilistic models.
Kernel function used is squared exponential based on the data distribution.
The residual error varies between ±95kN with high density of points seen around ±25kN.
EBT
ANN
LPR
TM
EDA
GPR
SVR
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Actual data
Prediction
σ Deviation
Two points are far apart and uncertainty is very high.
Two points have close covariance and uncertainty is low.
σ
Upper bound of CI
Lower bound of CI

## Slide 17: Ensemble Bagged Tree
A bagged ensemble tree is a machine learning algorithm where multiple tree models are trained to solve the same problem and combined to get better results.
Bagged ensembles help to avoid the problem of overfitting.
The model becomes resilient to generating errors.
Residual error varying between ±90kN with high density of points seen around ±20kN .
EBT
ANN
LPR
TM
EDA
GPR
SVR
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Initial Dataset
Bootstrap 1
Subset 1
Tree Model 1
Prediction 1
Bootstrap 2
Subset 2
Tree Model 2
Prediction 2
Final Prediction
Bootstrap n
Subset n
Tree Model n
Prediction n

## Slide 18: Artificial Neural Network
To model a better nonlinear correlation between the displacements and the loads.
The model was built with 2 hidden layers with RELU as activation function.
EBT
ANN
LPR
TM
EDA
GPR
SVR
EBT
ANN
LPR
TM
EDA
SVR
GPR
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Inputs
Weights
Summation and bias
Activation
Output
Residual error varying between ±80kN with high density of points seen around ±20kN .

## Slide 19: RESULT STUDY
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 20: Result Study
The results of each model and its performance for each main bearing loads is discussed in dashboard which can be accessed using below link.
https://public.tableau.com/views/Thesisresults_dashboard_v3/Dashboard1?:language=en-US&publish=yes&:display_count=n&:origin=viz_share_link
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 21: Summary and Outlook
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet

## Slide 22: Summary and Outlook
Analysis of Regression Models for estimating the main bearing loads of wind turbine
Mithun Nagesh Shet
Summary:
  With approach presented in thesis, Regression models can estimate main bearing loads from displacement values with certain degree of error.
  Apart from linear model, all models could capture nonlinearity due to bearing surface and clearance with Bagged ensemble showing highest robustness.
  Bagged Tree ensemble model consistently showed strong robustness for all main bearing loads.
  ANN model showed good performance with original dataset and captured nonlinearity but was inconsistent in robustness test.
  Compromise made between the accuracy and robustness.
Outlook:
  Models can be further trained with dataset consisting all kinds of error for better performance to capture nonlinearities.
  Further study is needed on the minimum threshold for accuracy and robustness required to be implemented in real world.